An Updated Photochemical Mechanism for Modeling Urban and Regional Air Quality:
Carbon Bond, Version 5 (CB-V)

4 December 2002

Prepared by:

Systems Applications International, Inc. (SAI) ICF Consulting 101 Lucas Valley Road, Suite 230 San Rafael, CA 94903 (415) 507-7164 JHaney@icfconsulting.com

Copyright 2002 by Systems Applications International, Inc.,

a subsidiary of ICF Consulting Group, Inc.

Table of Contents

Introduction	1

Highlights of CB-V	1

Background	3

Carbon Bond, Version 5 (CB-V, Version 1.0)	4

Demonstration of CB-V as Used in the UAM-V	4

Conclusion	5

References	6

List of Figures

Figure 1. GCOS UAM-V modeling domain. Horizontal grid resolution is approximately 36 km 
for Grid 1, 12 km for Grid 2, 4 km for Grids A, B, and C, and 2 km for Grid D.	20

Figure 2. Hourly ozone concentrations (ppb): CB-V vs. CB-IVtox for September 13–16, 1997	21

List of Tables

Table 1. Carbon Bond Mechanism, Version 5 (CB-V)	9

Table 2. Species Naming Conventions in CB-V	13

Table 6-2a. Summary of model performance metrics and statistics for 1-hour ozone for the 
12 km UAM-V modeling domain (Grid 2): base-case simulation.	14

Table 6-2d. Summary of model performance metrics and statistics for 1-hour ozone for the 
4 km Gulf Coast UAM-V modeling subdomain (Grid C): base-case simulation.	15

Table 6-2e. Summary of model performance metrics and statistics for 1-hour ozone for the 
2 km Louisiana UAM-V modeling subdomain (Grid D): base-case simulation.	16

Table 6-2a—CB-V. Summary of model performance metrics and statistics for 1-hour ozone 
for the 12 km UAM-V modeling domain (Grid 2): base-case simulation.	17

Table 6-2d—CB-V. Summary of model performance metrics and statistics for 1-hour ozone for the 4 km Gulf Coast UAM-V modeling subdomain (Grid C): base-case simulation.	18

This page intentionally left blank.

# Introduction

The latest Carbon Bond mechanism, Version 5 (CB-V), is now ready for use. CB-V is another step in the progressive development of the carbon-bond approach for producing “economical” yet comprehensive chemical mechanisms for simulating the formation of secondary atmospheric pollutants. This latest version, without significantly impacting computer resources or previously completed ozone attainment demonstrations, updates and expands the reactions contained in the extensively applied CB-IV mechanism by drawing on the latest evaluations of atmospheric reactions. CB-V provides a scientifically current treatment of the atmospheric chemistry that governs, for any seasonal condition and continental location, the formation of ozone (and other oxidants), the inorganic and organic constituents of fine particles, and air toxicants as well as the deposition of acidic and toxic substances. CB-V is designed to address the effects of precursor air emissions on ozone, PM, air toxics, visibility, acid deposition and water quality. Additionally, CB-V retains the unique Carbon Bond features of carbon mass balance and the ability to consistently handle a wide variety of organic molecules.

In the remainder of this technical memorandum, we first present highlights of the considerations that led to CB-V, the process followed for its development and some of its key features. The memorandum then documents the evolution of CB-V, starting with the changes made to CB-IV and concluding with a tabular summary of the 120 reactions that comprise CB-V. The memorandum concludes with a summary of results obtained using CB-V in UAM-V for an ozone simulation of a 14-state southeast region over a 9-day period (September 10—18, 1997).

# Highlights of CB-V

Builds on the success of CB-IV. CB-V extends the capability of CB-IV while remaining compatible with model-ready databases developed using CB-IV. Since its publication in 1989, CB-IV has been installed in many air quality models to simulate ozone formation throughout more than 50 metropolitan regions at all latitudes worldwide and for more than 150 different historical ozone episodes. These models have been the focus of manifoldly successful air quality planning projects. CB-V is compatible with those simulations.

Addresses published critiques of CB-IV. Two separate articles (Hess et al.; 1992 and Siminaitis et al.; 1997) report that simulated ozone concentrations in smog chamber experiments are low compared to the observed concentrations under the lowest ratios of initial VOC to NOx concentrations. This apparent bias disappears in CB-V when the single aldehyde in CB-IV is replaced with two aldehydes: acetaldehyde and a surrogate for “higher” aldehydes. Another critique of CB-IV (Luecken, et al, 1999) noted that an intermediate radical species in aromatics chemistry could accumulate at low NOx conditions. CB-V incorporates a reaction between this intermediate radical species and the hydroperoxy radical to resolve this issue.

Up-to-date. Care has been taken to assure that CB-V is consistent with all currently available reviews of evaluated reactions for use in modeling atmospheric chemistry.

Retains the unique carbon mass balance feature of CB-IV. Unlike many other mechanisms, the Carbon Bond approach accounts for and conserves virtually all active carbon atoms available for smog formation from emissions through the chemistry all the way to formation of CO2. This feature is not only important for long time scales with transport over long distances, it is also important for comparing total ambient VOC data with simulated data at specific locations. The separation of three types of olefin bonds and two types of aromatics is also preserved in the Carbon Bond chemistry so that these generic classes of compounds can be compared with ambient measurements.

Employs a new NOx species to assure conservation of nitrogen and computational efficiency. The chemistry solvers used in many air quality models utilize quasi-steady-state-approximations for species such as NO3 and N2O5. However, under some conditions these species can typically cause either mass balance problems under some conditions or so-called “stiff” computational problems under other conditions. Quasi-steady-state can avoid the former but create the latter problem. A new species, which is also used in REMSAD, avoids both the stiffness and mass-balance problems simultaneously.

Extends the unique ability of Carbon Bond chemistry to handle molecules with multiple chemistries. Many VOC molecules have multiple reaction paths in the atmosphere: a molecule like styrene, for example, reacts like an olefin and an aromatic molecule. The Carbon Bond approach provides for both reaction paths. Other mechanisms, such as SAPRC or RADM, require that it (styrene) be treated as either an olefin or an aromatic molecule. The result is that some of the chemistry of styrene is lost, some of the carbon mass is either lost or gained (depending on the choice) and emissions processing has a special rule for styrene. CB-V, by increasing the number of species used in CB-IV, expands the number of possible ways to treat the variety of chemistries and reactivities found in current VOC inventories while conserving carbon mass and allowing the use of the same CB-IV emissions processing software.

Provides explicit treatment of key toxic compounds. The compounds 1,3 butadiene, benzene, formaldehyde, and acetaldehyde have special regulatory significance and are now explicitly treated; other explicit compounds can be added as needed.

Allows for separate anthropogenic and biogenic inventories. CB-V treats all biogenic emissions with two separate primary species (one for isoprene and one for terpenes), while all other primary species are considered anthropogenic. This Carbon Bond chemistry is also currently used in the REMSAD model.

Designed for the “one atmosphere” concept: To simulate in one model the effects of air emissions on ozone, PM, air toxics, visibility, acid deposition and water quality. Inorganic and organic reactions have been added to CB-V (compared to CB-IV and other mechanisms), which are important for simulating surface-ozone and other oxidants under any seasonal conditions. CB-V contains the same inorganic chemistry as in REMSAD and UAM-VPM, and inorganic and organic chemistries are suitable for all seasons and regions of the troposphere.

Recognizes SO2, like CO, as a precursor of ozone formation. SO2, like CO, is oxidized in the atmosphere by its reaction with the hydroxyl radical, which is regenerated to form sulfate. Reducing SO2 emissions, like reducing CO emissions, will lower ozone concentrations in ozone attainment demonstrations when CB-V is used with an inventory of SO2 emissions.

Uses rate expressions that permit simulations over a wide range of pressures and temperatures. CB-V, unlike CB-IV, uses the equivalent of rate expressions rather than simple rate constants so that rate coefficients are suitable for all (urban, suburban, rural and remote) regions and seasons of the troposphere that might be encountered during an annual regional or continental simulation.

Does not significantly affect currently approved SIP programs or those in development. A recently completed simulation of a 9-day period over a 14-southeastern state region demonstrates that peak hourly ozone concentrations simulated with CB-V are within 5% of the corresponding values simulated with CB-IV when hourly values are between 100 to 124 ppb.

Does not significantly increase computational times. Recently completed comparisons between CB-V and CB-IV in a UAM-V multi-day, regional simulation show that computational times when CB-V is used are within 5% of those obtained when CB-IV is used.

Does not impact emissions inventory processing. CB-V uses virtually identical emissions processing software used for recent versions of CB-IV.

# Background

Since the original publication of the CB-IV mechanism (Gery et al, 1989), there have been several reports of revisions to CB-IV. These changes, among others, are incorporated into CB-V.

The revisions leading up to CB-V included updates to the peroxyacetyl nitrate (PAN) chemistry (see Gery, 1994), additions to the radical-radical reactions (see Gery, 1994, and Yarwood and Burton, 1993), and new reactions for isoprene chemistry (see Whitten et al., 1996) based on the work of Carter (1996). Adelman (1999) provides extensive documentation of most of the revisions to the first versions of CB-IV. Several of the original reports are available at the indicated web site. Moreover, Adelman has tested several of these revisions against some of the latest smog chamber experiments.

Ligocki et al. (1992) extended CB-IV to explicitly treat several toxic species. This version, known as CB-IVtox, was initially used to assess urban concentrations of air toxics (viz., benzene, 1,3 butadiene, formaldehyde and acetaldehyde) from vehicle emissions. Ligocki et al. found that the most extensive changes to the organic chemistry of CB-IV (Gery et al., 1989) followed from the requirement to explicitly treat the toxic species acetaldehyde. In the original CB-IV, acetaldehyde was used as a surrogate species for all aldehydes with more than one carbon atom and internal olefins (which quickly react to form higher aldehydes). The explicit treatment of acetaldehyde in CB-IVtox alone necessitated the introduction of three new species: ALDX, a surrogate for aldehydes having 3 or more carbons atoms; PANX, a surrogate for PAN-like compounds with three or more carbons; and IOLE, to represent internal olefin bonds.

Initially, the modifications made by Ligocki et al. were believed not to have affected simulated ozone concentrations. Subsequently, however, it was discovered that higher aldehydes (i.e., more than two carbon atoms) photolyzed significantly faster than acetaldehyde to produce radicals (Heiklen et al., 1986, and Martinez et al., 1992), which would increase the formation of ozone. This indicated that while acetaldehyde may have been a poor surrogate to represent the higher aldehydes it (surrogate acetaldehyde) may also have provided too few radicals at the lowest VOC to NOx ratios. Coincidentally, two independent published studies (Simonaitis, Meagher, and Bailey, 1997, and Hess et al., 1992) claimed that the original CB-IV mechanism understated ozone concentrations at the lowest VOC to NOx ratios when tested against smog chamber data using comprehensive urban-like mixtures of VOC. The smog chamber database used by Gery et al. (1989) did not have similarly very low VOC to NOx ratios, and neither the individual organic compounds nor the various urban mixtures used to test the performance of the chemistry specifically addressed aldehydes higher than acetaldehyde. Hence, serendipitously, the revisions made by Ligocki et al. (1992) to treat acetaldehyde as an explicit toxic species, resulted in increasing ozone production, but only at the lowest VOC to NOx ratios where, according to the experiments of Hess et al. and Siminaitis et al., more ozone was needed. Ironically, Zaveri and Peters (1999), in publishing their revisions to CB-IV, incorporated some of the changes made by Ligocki et al. (such as IOLE) but unfortunately did not expand the carbonyls to separately address the higher aldehydes.

Another noteworthy study leading to CB-V is the work of Liang and Jacobson (2000), who compared the organic part of CB-IV against a 4,000-reaction mechanism used in European modeling. The inorganic reaction set used by Liang and Jacobson was the same for both the organic-CB-IV and the 4,000-reaction set. The CB-V provided in this memorandum also has some additions to the inorganic reaction set to be consistent with the work of Liang and Jacobson. For the most part, both the 4,000-reaction and CB-IV-reaction mechanisms gave similar results when used to simulate urban smog episodes. Liang and Jacobson noted significant differences, however, when the urban mixtures of volatile organic compounds (VOC) contained high concentrations of aromatic compounds. When mixtures were rich in aromatics, the CB-IV reaction mechanism was better at reproducing the observed ozone profiles than was the 4000-reaction mechanism. The ability of CB-IV to reproduce experiments with large amounts of aromatics is probably attributable to the empirically derived aromatic chemistry used in the original development of CB-IV (Gery et al. [1989]).

# Carbon Bond, Version 5 (CB-V, Version 1.0)

A complete and detailed list of CB-V is provided in Table 1. (see end of memorandum for Tables). All inorganic and organic reactions are included. Table 2 lists the names of state and steady-state species used when CB-V is installed into UAM-V.

## Demonstration of CB-V as Used in the UAM-V

The current version of CB-V has been installed into the UAM-V (v. 1.31) photochemical grid model and that model has been exercised for a multiday episode on a regional grid (see Figure 1), which was used in the 1-hour SIP-extension modeling analysis for Baton Rouge (Douglas et al., 2001). The chemistry used in the SIP was the CB-IV (the CB4-tox version). Although the full SIP modeling exercise involved three meteorological episodes, the CB-V demonstration involved modeling of one episode (September, 1997). The original performance statistics for the SIP work are reproduced here from Tables 6-2a, 6-2d, and 6-2e of Douglas et al. Figure 1 shows the modeling region and the localized grid regions mentioned in these tables. As can be seen in these tables, the original mechanism (plus inventory, wind model, etc.) performed well enough to be used in the SIP. Shaded areas show where the results did fail to meet the EPA recommended ranges for acceptable model performance.

Using the new CB-V chemistry (keeping everything else the same as used in the SIP modeling), the new performance results are presented in the tables labeled Table 6-2a—CB-V, Table 6-2d—CB-V, and Table 6-2e—CB-V. The results are similar, and marginally better. For example, as presented in Table 6-2a (12-km grids), modeling with CB-IVtox achieves EPA’s performance targets for five of the nine days Table 6-2a (non-shaded table entries); when CB-V was used, EPA’s performance targets were achieved on six days, a 20 percent improvement (Table 2a-CB-V, shaded entries). Similar improvements were achieved for the 4 km and 2 km grid resolutions (Tables 6-2d and Tables 6-2e, respectively). Comparing the results in Table 6-2d with those in Table 6-2d-CB-V shows that the number of days when the bias target is met increases from 7 to 8. Comparing the results for 2 km grid resolution (Table 6-2e with those in Table 6-2e-CB-V) shows that all of EPA’s performance targets are achieved when CB-V was used (there are no shaded entries in Table 6-2e-CB-V). Therefore, in the region critical and specific to the SIP (Grid D, with 2 km resolution)) the original Table 6-2e showed the modeling failed to achieve EPA’s performance target on one day but with CB-V all days exceeded EPA’s performance targets.

In other measures of performance (other than the number of cases that do not achieve EPA’s targets), the simulated ozone obtained using CB-V and CB-IVtox is very similar. However, when differences do occur they are most often in the direction of somewhat better performance for CB-V than CB-IVtox when the results of each are compared to observations.

Figure 2 presents a comparison of all simulated hourly ozone concentrations of CB-IVtox with CB-V in all grid cells in which there are ozone monitors for September 14, 15, 16 and 17, 1997. The simulations are virtually perfectly correlated, indicating once again that the enhancements included in CB-V, while advancing its credibility and utility (to a broader range of conditions), do not appear to impact decisions previously made with CB-IV.

# Conclusion

There are three conclusions that follow from this demonstration.

- CB-V has been installed and tested in the latest version of UAM-V (v. 1.31). The UAM-V is now ready to simulate other regions and episodes using the most recent chemistry available.

- CB-V gives very similar results to CB-IVtox. Although box-model simulations have shown that either CB-IVtox or CB-V estimate higher peak ozone concentrations than the initial version of CB-IV at low VOC to NOx conditions, all three versions now generally appear to give similar results.

Because CB-V is close in performance to CB-IVtox and apparently CB-IV most of the time, past (SIP) ozone attainment demonstrations or other important studies using CB-IV or CB4-tox are not threatened or rendered significantly obsolete by this new chemistry.

# References

Adelman, Z.E. 1999 “A Reevaluation of the Carbon Bond-IV Photochemical Mechanism” Master of Science Thesis, School of Public Health, University of North Carolina, Chapel Hill, NC, available at http://airsite.unc.edu/soft/cb4/CB4docs.html.

Atkinson, R., H.E. Jeffries, G.Z. Whitten, F.W. Lurmann, and B. Dimitriades 1987 “Workshop on Evaluation/Documentation of Chemical Mechanisms,” U.S. EPA/600/9-87/024.

Atkinson, R. 1994 “Gas-Phase Tropospheric Chemistry of Organic Compounds,” Journal of Physical and Chemical Reference Data, Monograph No. 2, page 47.

Atkinson, R. 1997 “Gas-Phase Tropospheric Chemistry of Volatile Organic Compounds: 1. Alkanes and Alkenes,” Journal of Physical and Chemical Reference Data, Vol. 26, page 215.

Atkinson, R., D.L. Baulch, R.A. Cox, R.F. Hampson, Jr., J.A. Kerr, M.J. Rossi, and J. Troe 1997 “Evaluated Kinetic, Photochemical and Heterogeneous Data for Atmospheric Chemistry: Supplement V, IUPAC Subcommittee on Gas Kinetic Data Evaluation for Atmospheric Chemistry,” Journal of Physical and Chemical Reference Data, Vol. 26, pp 521-1013.

Calvert, J.G., G. Yarwood, and A.M. Dunker 1994 “An Evaluation of the Mechanism of Nitrous Acid Formation in the Urban Atmosphere,” Res. Chem. Intermed, Vol. 20, pp 463-502.

Carter, W.P.L. 1996 “Condensed Atmospheric Photochemical Mechanisms for Isoprene,” Atmospheric Environment, Vol. 30, pp 4275-4290.

DeMore, W.B., S.P. Sander, C.J. Howard, A.R. Ravishankara, D.M. Golden, C.E. Kolb, R.F. Hampson, M.J. Kurylo, and M.J. Molina 1997 “Chemical Kinetics and Photochemical Data for Use in Stratospheric Modeling: Evaluation Number 12,” JPL Publication 97-4, NASA.

Douglas, S.G., A.B. Hudischewskyj, Y.H. Wei, R.S. Beizaie, A.R. Alvarez, and J.L. Haney 2001 “Technical Support Document: 1-Hour Ozone Attainment Demonstration Modeling for Baton Rouge,” Systems Applications International/ICF Consulting, San Francisco, CA. Report #01-066.

Gery, M.W. 1994 “Summary of Revisions and Versions of the CBM-4 Mechanism,” Technical Memorandum of Atmospheric Research Associates, Boston, MA, March 29, also available as Docket #1 at http://airsite.unc.edu/soft/cb4/CB4docs.html.

Gery, M.W., G.Z. Whitten, J.P. Killus, and M.C. Dodge 1989 “A Photochemical Kinetics Mechanism for Urban and Regional Computer Modeling,” Journal of Geophysical Research, Vol. 94, pp 12,925-12,956.

Harrison, R.M, J.D. Peak, and G.M Collins 1994 “Tropospheric cycle of nitrous acid,” Journal of Geophysical Research, Vol.101, pp 14,429-14,439.

Heiklen, J., J. Desai, A. Bahta, C. Harper, and R. Simonaitis 1992 “The temperature and wavelength dependence o the photooxidation of propionaldehyde,” Journal of Photochemistry, Vol. 34, pp 117-135.form

Hess, G.D., F. Carnovale, M.E. Cope, and G.M. Johnson 1992 “The Evaluation of Some Photochemical Smog Reaction Mechanisms,” Atmospheric Environment, Vol. 26A, pp 625-659.

Hough, A.M. 1991 “Development of a two-dimensional global tropospheric model: model chemistry,” Journal of Geophysical Research, Vol. 96, pp 7325-7362.

Liang, J, and M.Z. Jacobson 2000 “Comparison of a 4000-reaction chemical mechanism with the carbon bond IV and adjusted carbon bond IV-EX mechanism using SMVGEAR II,” Atmospheric Environment, Vol. 34, pp 3015.

Luecken, D.J., G.S. Tonnesen, and J.E. Sickles 1999 “Differences in NOy speciation predicted by three photochemical mechanisms,” Atmospheric Environment, Vol. 33, pp 1073-1084.

Ligocki, M.P., R.R. Schulhof, R.E. Jackson, M.M. Jimenez, G.Z. Whitten, G.M. Wilson, T.C. Myers, and J.L. Fieber 1992 “Modeling the Effects of Reformulated Gasolines on Ozone and Toxics Concentrations in the Baltimore and Houston Areas,” Final Report SYSAPP-92/127 to U.S. EPA, Systems Applications International, San Rafael, California.

Martinex, R.D., A.A. Buitrago, N.W. Howell, C.H. Hearn, and J.A. Joens 1992 “The near U.V. absorptio spectra of several aliphatic aldehydes and detones at 300K,” Atmospheric Environment, Vol. 26A, pp 785-792.

Sander, S.P., R.R. Friedl, W.B. DeMore, A.R. Ravishankara, D.M. Golden, C.E. Kolb, M.J. Kurylo, R.F. Hampson, R.E. Huie, M.J. Molina, and G.K. Moortgat 2000 “Chemical Kinetics and Photochemical Data for Use in Stratospheric Modeling: Evaluation Number 13,” JPL Publication 00-3, NASA.

Simonaitis, R., J.F. Meagher, and E.M. Bailey 1997 “Evaluation of the Condensed Carbon Bond (CB-IV) Mechanism Against Smog Chamber Data at Low VOC and NOx Concentrations,” Atmospheric Environment, Vol. 31, pp 27-43.

Stockwell, W.R., P. Middleton, and J.S. Chang 1990 “The second generation regional acid deposition model chemical mechanism for regional air quality modeling,” Journal of Geophysical Research, Vol. 95, pp 16,343-16,367.

Whitten, G.Z., H. Hogo, and J.P. Killus 1980 “The Carbon-Bond Mechanism: A Condensed Kinetic Mechanism for Photochemical Smog,” Environmental Science and Technology, Vol. 14, pp 690-700.

Whitten, G.Z., H.P. Duel, C.S. Burton, J.L. Haney 1996 “Overview of the Implementation of an Updated Isoprene Chemistry Mechanism in CB4/UAM-V,” Technical Memorandum of Systems Applications International, Inc., San Rafael, CA., also available as Docket #5 at http://airsite.unc.edu/soft/cb4/CB4docs.html.

Whitten, G.Z., D. Gao, and J.P. Killus 1998 “Effect of Chemical Mechanism Uncertainty on Airshed Model Results,” Final Reports (Phases 1 and II) to California Air Resources Board, SYSAPP-97/57 and SYSAPP-98/21, Systems Applications International, Inc., San Rafael, CA, 1998.

Yarwood, G. and S. Burton 1993 “An Update to the Radical-Radical Termination Reactions in the CBM-IV,” Technical Memorandum of Systems Applications International, Inc., San Rafael, CA, December 27, also available as Docket #3 at http://airsite.unc.edu/soft/cb4/CB4docs.html.

Zaveri, R.A., L.K. Peters 1999 “A new lumped structure photochemical mechanism for large-scale applications,” Journal of Geophysical Research, Vol. 104, pp 30,387-30,400

Table 1. Carbon Bond Mechanism, Version 5 (CB-V)

(See Note at end of table for information about symbols and names

| Number | Reactants |  |  |  |  |  |  | Products |  |  |  |  |  |  |  |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 1 | NO2 | + | h( |  |  | ===> |  | NO | + |  | O | – |  | NOXY |  |  |  |  |  |  |
| 2 | O | + | P |  |  | ===> |  | O3 | + |  | P |  |  |  |  |  |  |  |  |  |
| 3 | O3 | + | NO |  |  | ===> |  | NO2 | + |  | NOXY |  |  |  |  |  |  |  |  |  |
| 4 | O3 | + | NO2 |  |  | ===> |  | NO3 |  |  |  |  |  |  |  |  |  |  |  |  |
| 5 | O3 | + | OH |  |  | ===> |  | HO2 |  |  |  |  |  |  |  |  |  |  |  |  |
| 6 | O3 | + | HO2 |  |  | ===> |  | OH |  |  |  |  |  |  |  |  |  |  |  |  |
| 7 | O3 | + | NO3 |  |  | ===> |  | NO2 |  |  |  |  |  |  |  |  |  |  |  |  |
| 8 | O3 | + | h( |  |  | ===> |  | O |  |  |  |  |  |  |  |  |  |  |  |  |
| 9 | O3 | + | h( |  |  | ===> |  | O1D |  |  |  |  |  |  |  |  |  |  |  |  |
| 10 | NO | + | NO |  |  | ===> | 2 | NO2 | + | 2 | NOXY |  |  |  |  |  |  |  |  |  |
| 11 | NO | + | NO2 | + | H2O | ===> | 2 | HNO2 | – |  | NOXY |  |  |  |  |  |  |  |  |  |
| 12 | NO | + | O | + | P | ===> |  | NO2 | + |  | P | + |  | NOXY |  |  |  |  |  |  |
| 13 | NO | + | OH | + | P | ===> |  | HNO2 | + |  | P |  |  |  |  |  |  |  |  |  |
| 14 | NO | + | HO2 |  |  | ===> |  | NO2 | + |  | OH |  |  |  |  |  |  |  |  |  |
| 15 | NO | + | XO2 |  |  | ===> |  | NO2 | + |  | NOXY |  |  |  |  |  |  |  |  |  |
| 16 | NO | + | XO2N |  |  | ===> |  | NTR |  |  |  |  |  |  |  |  |  |  |  |  |
| 17 | NO | + | NO3 |  |  | ===> | 2 | NO2 | + |  | NOXY |  |  |  |  |  |  |  |  |  |
| 18 | NO2 | + | O |  |  | ===> |  | NO | – |  | NOXY |  |  |  |  |  |  |  |  |  |
| 19 | NO2 | + | O | + | P | ===> |  | NO3 | + |  | P |  |  |  |  |  |  |  |  |  |
| 20 | NO2 | + | OH | + | P | ===> |  | HNO3 | + |  | P | – |  | NOXY |  |  |  |  |  |  |
| 21 | NO2 | + | HO2 | + | P | ===> |  | PNA | + |  | P | – |  | NOXY |  |  |  |  |  |  |
| 22 | NO2 | + | NO3 |  |  | ===> |  | NO | + |  | NO2 | – |  | NOXY |  |  |  |  |  |  |
| 23 | NO2 | + | NO3 |  |  | ===> | 2 | NO2 |  |  |  |  |  |  |  |  |  |  |  |  |
| 24 | NO2 | + | NO3 | + | P | ===> |  | N2O5 | + |  | P |  |  |  |  |  |  |  |  |  |
| 25 | HNO2 | + | HNO2 |  |  | ===> |  | NO | + |  | NO2 | + |  | NOXY |  |  |  |  |  |  |
| 26 | HNO2 | + | OH |  |  | ===> |  | NO2 | + |  | NOXY |  |  |  |  |  |  |  |  |  |
| 27 | HNO2 | + | h( |  |  | ===> |  | NO | + |  | OH |  |  |  |  |  |  |  |  |  |
| 28 | HNO3 | + | OH | + | P | ===> |  | NO3 | + |  | P | + |  | NOXY |  |  |  |  |  |  |
| 29 | PNA | + | OH |  |  | ===> |  | NO2 | + |  | NOXY |  |  |  |  |  |  |  |  |  |
| 30 | PNA |  |  |  |  | ===> |  | HO2 | + |  | NO2 | + |  | NOXY |  |  |  |  |  |  |
| 31 | PNA | + | h( |  |  | ===> | 0.61 | HO2 | + | 0.61 | NO2 | + | 0.39 | OH | + | 0.39 | NO3 | + |  | NOXY |
| 32 | N2O5 | + | H2O |  |  | ===> | 2 | HNO3 | – | 2 | NOXY |  |  |  |  |  |  |  |  |  |
| 33 | N2O5 |  |  |  |  | ===> |  | NO3 | + |  | NO2 |  |  |  |  |  |  |  |  |  |
| 34 | H2O2 | + | OH |  |  | ===> |  | HO2 |  |  |  |  |  |  |  |  |  |  |  |  |
| 35 | H2O2 | + | h( |  |  | ===> | 2 | OH |  |  |  |  |  |  |  |  |  |  |  |  |
| 36 | O1D | + | P |  |  | ===> |  | O | + |  | P |  |  |  |  |  |  |  |  |  |

| Table 1. Carbon Bond Mechanism, Version 5 (CB-V) (continued) |
| --- |
| Number | Reactants |  |  |  |  |  |  | Products |  |  |  |  |  |  |  |  |  |  |  |  |
| 37 | O1D | + | H2O |  |  | ===> | 2 | OH |  |  |  |  |  |  |  |  |  |  |  |  |
| 38 | CO | + | OH |  |  | ===> |  | HO2 |  |  |  |  |  |  |  |  |  |  |  |  |
| 38 | CO | + | OH | + | P | ===> |  | HO2 | + |  | P |  |  |  |  |  |  |  |  |  |
| 39 | H2 | + | OH |  |  | ===> |  | HO2 | + |  | H2O |  |  |  |  |  |  |  |  |  |
| 40 | HO2 | + | OH |  |  | ===> |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| 41 | HO2 | + | HO2 |  |  | ===> |  | H2O2 |  |  |  |  |  |  |  |  |  |  |  |  |
| 41 | HO2 | + | HO2 | + | P | ===> |  | H2O2 | + |  | P |  |  |  |  |  |  |  |  |  |
| 42 | HO2 | + | HO2 | + | H2O | ===> |  | H2O2 |  |  |  |  |  |  |  |  |  |  |  |  |
| 42 | HO2 | + | HO2 | + | H2O(P) | ===> |  | H2O2 |  |  |  |  |  |  |  |  |  |  |  |  |
| 43 | HO2 | + | XO2 |  |  | ===> |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| 44 | HO2 | + | XO2N |  |  | ===> |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| 45 | XO2 | + | XO2 |  |  | ===> |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| 46 | XO2 | + | XO2N |  |  | ===> |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| 47 | XO2N | + | XO2N |  |  | ===> |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| 48 | NO3 | + | OH |  |  | ===> |  | HO2 | + |  | NO2 |  |  |  |  |  |  |  |  |  |
| 49 | NO3 | + | HO2 |  |  | ===> |  | HNO3 | – |  | NOXY |  |  |  |  |  |  |  |  |  |
| 50 | NO3 | + | NO3 |  |  | ===> | 2 | NO2 |  |  |  |  |  |  |  |  |  |  |  |  |
| 51 | NO3 | + | h( |  |  | ===> | 0.89 | NO2 | + | 0.89 | O | + | 0.11 | NO | – | 0.1 | NOXY |  |  |  |
| 52 | FORM | + | O |  |  | ===> |  | OH | + |  | HO2 | + |  | CO |  |  |  |  |  |  |
| 53 | FORM | + | OH |  |  | ===> |  | HO2 | + |  | CO |  |  |  |  |  |  |  |  |  |
| 54 | FORM | + | NO3 |  |  | ===> |  | HNO3 | + |  | HO2 | + |  | CO | – |  | NOXY |  |  |  |
| 55 | FORM | + | h( |  |  | ===> |  | HO2 | + |  | CO |  |  |  |  |  |  |  |  |  |
| 56 | FORM | + | h( |  |  | ===> |  | CO |  |  |  |  |  |  |  |  |  |  |  |  |
| 57 | ACET | + | O |  |  | ===> |  | C2O3 | + |  | OH |  |  |  |  |  |  |  |  |  |
| 58 | ACET | + | OH |  |  | ===> |  | C2O3 |  |  |  |  |  |  |  |  |  |  |  |  |
| 59 | ACET | + | NO3 |  |  | ===> |  | C2O3 | + |  | HNO3 | – |  | NOXY |  |  |  |  |  |  |
| 60 | ACET | + | h( |  |  | ===> |  | FORM | + | 2 | HO2 | + |  | CO | + |  | XO2 |  |  |  |
| 61 | O | + | ALDX |  |  | ===> |  | CXO3 | + |  | OH | – | 1 | PAR |  |  |  |  |  |  |
| 62 | OH | + | ALDX |  |  | ===> |  | CXO3 | - | 1 | PAR |  |  |  |  |  |  |  |  |  |
| 63 | NO3 | + | ALDX |  |  | ===> |  | CXO3 | + |  | HNO3 | – | 1 | PAR | – |  | NOXY |  |  |  |
| 64 | ALDX | + | h( |  |  | ===> |  | ACET | + | 2 | HO2 | + |  | CO | + |  | XO2 | – | 1.0 | PAR |
| 65 | C2O3 | + | NO |  |  | ===> |  | FORM | + |  | NO2 | + |  | HO2 | + |  | XO2 | + |  | NOXY |
| 66 | C2O3 | + | NO2 |  | P | ===> |  | PAN | + |  | P | – |  | NOXY |  |  |  |  |  |  |
| 67 | C2O3 | + | HO2 |  |  | ===> | 0.26 | O3 |  |  |  |  |  |  |  |  |  |  |  |  |
| 68 | C2O3 | + | C2O3 |  |  | ===> | 2 | FORM | + | 2 | XO2 | + | 2 | HO2 |  |  |  |  |  |  |
| 69 | CXO3 | + | NO |  |  | ===> |  | ACET | + |  | NO2 | + |  | HO2 | + |  | XO2 | + |  | NOXY |
| 70 | CXO3 | + | NO2 |  |  | ===> |  | PANX | – |  | NOXY |  |  |  |  |  |  |  |  |  |
| 71 | CXO3 | + | HO2 |  |  | ===> | 0.33 | O3 |  |  |  |  |  |  |  |  |  |  |  |  |
| 72 | CXO3 | + | C2O3 |  |  | ===> |  | ACET | + |  | FORM | + | 2 | XO2 | + | 2.0 | HO2 |  |  |  |
| 73 | PAN |  |  |  |  | ===> |  | C2O3 | + |  | NO2 | + |  | NOXY |  |  |  |  |  |  |
| 74 | PANX |  |  |  |  | ===> |  | CXO3 | + |  | NO2 | + |  | NOXY |  |  |  |  |  |  |
| 75 | PANX | + | OH |  |  | ===> |  | ACET | + |  | NO2 | + |  | NOXY |  |  |  |  |  |  |
| 76 | CH4 | + | OH | + |  | ===> |  | FORM | + |  | XO2 | + |  | HO2 |  |  |  |  |  |  |
| 77 | PAR | + | OH |  |  | ===> | 0.87 | XO2 | + | 0.13 | XO2N | + | 0.11 | HO2 | – | 0.11 | PAR | + | 0.06 | ACET |
|  |  |  |  |  |  |  |  |  | + | 0.76 | ROR | + | 0.05 | ALDX |  |  |  |  |  |  |
| 78 | ROR |  |  |  |  | ===> | 0.96 | XO2 | + | 0.6 | ACET | + | 0.94 | HO2 | – | 2.1 | PAR | + | 0.04 | XO2N |
|  |  |  |  |  |  |  |  |  | + | 0.02 | ROR | + | 0.5 | ALDX |  |  |  |  |  |  |
| 79 | ROR |  |  |  |  | ===> |  | HO2 |  |  |  |  |  |  |  |  |  |  |  |  |
| 80 | ROR | + | NO2 |  |  | ===> |  | NTR | – |  | NOXY |  |  |  |  |  |  |  |  |  |
| 81 | ETH | + | O |  |  | ===> | 0.95 | FORM | + | 1.55 | HO2 | + | 0.95 | CO | + | 0.6 | XO2 | + | 0.35 | OH |
| 82 | ETH | + | OH | + | P | ===> |  | XO2 | + | 1.56 | FORM | + | 0.22 | ALDX | + |  | HO2 | + |  | P |
| 83 | ETH | + | O3 |  |  | ===> | 1.02 | FORM | + | 0.325 | CO | + | 0.08 | HO2 | + | 0.02 | H2O2 |  |  |  |
| 84 | OLE | + | O |  |  | ===> | 0.19 | ACET | + | 0.29 | HO2 | + | 0.19 | XO2 | + | 0.2 | CO | + | 0.2 | FORM |
|  |  |  |  |  |  |  |  |  | + | 0.007 | XO2N | + | 0.61 | PAR | + | 0.3 | ALDX |  |  |  |
| 85 | OLE | + | OH | + | P | ===> | 0.71 | FORM | + | 0.36 | ACET | + | 0.59 | ALDX | – | 0.71 | PAR | + | 0.71 | XO2 |
|  |  |  |  |  |  |  |  |  | + | 0.95 | HO2 |  |  |  |  |  |  |  |  |  |
| 86 | OLE | + | O3 |  |  | ===> | 0.2 | ACET | + | 0.86 | FORM | + | 0.45 | XO2 | – | 1 | PAR | + | 0.31 | OH |
|  |  |  |  |  |  |  |  |  | + | 0.395 | CO | + | 0.42 | HO2 | + | 0.32 | ALDX | + | 0.08 | H2O2 |
| 87 | OLE | + | NO3 |  |  | ===> | 0.91 | XO2 | + |  | FORM | + | 0.09 | XO2N | – | 1 | PAR | + | 0.35 | ACET |
|  |  |  |  |  |  |  |  |  | + | 0.56 | ALDX | + |  | NO2 |  |  |  |  |  |  |
| 88 | IOLE | + | O |  |  | ===> | 1.14 | ACET | + | 0.76 | ALDX | + | 0.1 | HO2 | + | 0.1 | XO2 | + | 0.1 | CO |
|  |  |  |  |  |  |  |  |  | + | 0.1 | PAR |  |  |  |  |  |  |  |  |  |
| 89 | IOLE | + | OH |  |  | ===> | 1.2 | ACET | + | 0.8 | ALDX | + |  | HO2 | + |  | XO2 |  |  |  |
| 90 | IOLE | – | O3 |  |  | ===> | 0.6 | ACET | + | 0.4 | ALDX | + | 0.25 | FORM | + | 0.25 | CO | + | 0.5 | O |
|  |  |  |  |  |  |  |  |  | + | 0.5 | OH | + | 0.5 | HO2 |  |  |  |  |  |  |
| 91 | IOLE | + | NO3 |  |  | ===> | 1.09 | ACET | + | 0.73 | ALDX | + |  | HO2 | + |  | NO2 |  |  |  |
| 92 | TOL | + | OH |  |  | ===> | 0.44 | HO2 | + | 0.08 | XO2 | + | 0.36 | CRES | + | 0.56 | TO2 |  |  |  |
| 93 | TO2 | + | NO |  |  | ===> | 0.9 | NO2 | + | 0.9 | HO2 | + | 0.9 | OPEN | + | 0.1 | XO2N | + | 0.9 | NOXY |
| 94 | TO2 |  |  |  |  | ===> |  | CRES | + |  | HO2 |  |  |  |  |  |  |  |  |  |
| 95 | CRES | + | OH |  |  | ===> | 0.4 | CRO | + | 0.6 | XO2 | + | 0.6 | HO2 | + | 0.30 | OPEN |  |  |  |
| 96 | CRES | + | NO3 |  |  | ===> |  | CRO | + |  | HNO3 | – |  | NOXY |  |  |  |  |  |  |
| 97 | CRO | + | NO2 |  |  | ===> |  | NTR | – |  | NOXY |  |  |  |  |  |  |  |  |  |
| 98 | CRO | + | HO2 |  |  | ===> |  | CRES |  |  |  |  |  |  |  |  |  |  |  |  |
| 99 | OPEN | + | OH |  |  | ===> |  | XO2 | + | 2 | CO | + | 2 | HO2 | + |  | C2O3 | + |  | FORM |
| 100 | OPEN | + | O3 |  |  | ===> | 0.03 | ALDX | + | 0.62 | C2O3 | + | 0.7 | FORM | + | 0.03 | XO2 | + | 0.69 | CO |
|  |  |  |  |  |  |  |  |  | + | 0.69 | CO | + | 0.08 | OH | + | 0.76 | HO2 | + | 0.2 | MGLY |
| 101 | OPEN |  |  |  |  | ===> |  | C2O3 | + |  | HO2 | + |  | CO |  |  |  |  |  |  |
| 102 | XYL | + | OH |  |  | ===> | 0.7 | HO2 | + | 0.5 | XO2 | + | 0.2 | CRES | + | 0.8 | MGLY | + | 1.1 | PAR |
|  |  |  |  |  |  |  |  |  |  |  |  | + | 0.3 | TO2 |  |  |  |  |  |  |
| 103 | MGLY | + | OH |  |  | ===> |  | XO2 | + |  | C2O3 |  |  |  |  |  |  |  |  |  |
| 104 | MGLY |  |  |  |  | ===> |  | C2O3 | + |  | HO2 | + |  | CO |  |  |  |  |  |  |
| 105 | ISOP | + | O |  |  | ===> | 0.25 | HO2 | + | 0.25 | XO2 | + | 0.75 | ISPD | + | 0.25 | CXO3 | + | 0.25 | PAR |
|  |  |  |  |  |  |  |  |  | + | 0.5 | FORM |  |  |  |  |  |  |  |  |  |
| 106 | ISOP | + | OH |  |  | ===> | 0.912 | ISPD | + | 0.991 | XO2 | + | 0.912 | HO2 | + | 0.629 | FORM | + | 0.088 | XO2N |
| 107 | ISOP | + | O3 |  |  | ===> | 0.6 | FORM | + | 0.65 | ISPD | + | 0.15 | ALDX | + | 0.2 | CXO3 | + | 0.35 | PAR |
|  |  |  |  |  |  |  |  |  | + | 0.266 | OH | + | 0.2 | XO2 | + | 0.066 | HO2 |  |  |  |
| 108 | ISOP | + | NO3 |  |  | ===> | 0.2 | ISPD | + |  | XO2 | + | 0.8 | HO2 | + | 0.2 | NO2 | + | 0.8 | ALDX |
|  |  |  |  |  |  |  |  |  | + | 2.4 | PAR | + | 0.8 | NTR | – | 0.8 | NOXY |  |  |  |
| 109 | ISOP | + | NO2 |  |  | ===> | 0.2 | ISPD | + |  | XO2 | + | 0.8 | HO2 | + | 0.2 | N0 | + | 0.8 | ALDX |
|  |  |  |  |  |  |  |  |  | + | 2.4 | PAR | + | 0.8 | NTR | – |  | NOXY |  |  |  |
| 110 | ISPD | + | OH |  |  | ===> | 0.334 | CO | + | 0.252 | ACET | + | 0.167 | FORM | + | 1.565 | PAR | + | 0.168 | MGLY |
|  |  |  |  |  |  |  |  |  | + | 0.503 | HO2 | + | 0.713 | XO2 | + | 0.21 | C2O3 | + | 0.5 | CXO3 |
| 110 | ISPD | + | OH |  |  | ===> | 0.334 | CO | + | 0.252 | ACET | + | 0.167 | FORM | + | 1.565 | PAR | + | 0.168 | MGLY |
|  |  |  |  |  |  |  |  |  | + | 0.503 | HO2 | + | 0.713 | XO2 | + | 0.21 | C2O3 | + | 0.24 | ALDX |
| 111 | ISPD | + | O3 |  |  | ===> | 0.02 | ACET | + | 0.15 | FORM | + | 0.225 | CO | + | 0.85 | MGLY | + | 0.36 | PAR |
|  |  | + |  |  |  |  |  |  | + | 0.114 | C2O3 | + | 0.064 | XO2 | + | 0.268 | OH | + | 0.154 | HO2 |
| 112 | ISPD | + | NO3 |  |  | ===> | 0.643 | CO | + | 0.282 | FORM | + | 0.357 | ALDX | + | 1.282 | PAR | + | 0.925 | HO2 |
|  |  | + |  |  |  |  |  |  | + | 0.075 | CXO3 | + | 0.075 | XO2 | + | 0.85 | NTR | + | 0.075 | HNO3 |
| 113 | ISPD |  |  |  |  | ===> | 0.333 | CO | + | 0.067 | ACET | + | 0.9 | FORM | + | 0.832 | PAR | + | 1.033 | HO2 |
|  |  | + |  |  |  |  |  |  | + | 0.7 | XO2 | + | 0.267 | C2O3 | + | 0.7 | CXO3 |  |  |  |
| 114 | TERP | + | O |  |  | ===> | 0.15 | ALDX | + | 0.51 | PAR |  |  |  |  |  |  |  |  |  |
| 115 | TERP | + | OH |  |  | ===> | 0.75 | HO2 | + | 1.25 | XO2 | + | 0.25 | XO2N | + | 0.28 | FORM | + | 0.47 | ALDX |
| 116 | TERP | + | O3 |  |  | ===> | 0.57 | OH | + | 0.07 | HO2 | + | 0.76 | XO2 | + | 0.18 | XO2N | + | 0.24 | FORM |
|  |  | + |  |  |  |  |  |  | + | 0.001 | CO | + | 7 | PAR | + | 0.21 | ALDX | + | 0.39 | CXO3 |
| 117 | TERP | + | NO3 |  |  | ===> | 0.47 | NO2 | + | 0.28 | HO2 | + | 1.03 | XO2 | + | 0.25 | XO2N | + | 0.47 | ALDX |
|  |  |  |  |  |  |  |  |  | + | 0.53 | NTR | – | 0.53 | NOXY |  |  |  |  |  |  |
| 118 | SO2 | + | OH |  |  | ===> |  | SULF | + |  | HO2 |  |  |  |  |  |  |  |  |  |
| 119 | SO2 |  |  |  |  | ===> |  | SULF |  |  |  |  |  |  |  |  |  |  |  |  |
| 120 | ETOH | + | OH |  |  | ===> | 0.95 | ACET | + | 0.1 | XO2 | + |  | HO2 | + | 0.1 | FORM |  |  |  |

Note: P in these expressions denotes a pressure dependent reaction. The chemical names of reactants and products are presented in Table 2.

Table 2. Species Naming Conventions in CB-V

| State Species | Description |
| --- | --- |
| NO | Nitric Oxide |
| NO2 | Nitrogen Dioxide |
| O3 | Ozone |
| OLE | Terminal olefin bond (2 carbons) |
| PAR | Paraffinic bond (1 carbon) |
| TOL | Toluene (7 carbons) |
| XYL | Xylene (8 carbons) |
| FORM | Formaldehyde (secondary, 1 carbon) |
| ACET | Acetaldehyde (secondary, 2 carbons) |
| ETH | Ethene (2 carbons) |
| CRES | Cresol (7 carbons) |
| MGLY | Methyl Glyoxal (2 carbons) |
| OPEN | Aromatic Product |
| PNA | Peroxynitric Acid |
| PAN | Peroxyacetyl Nitrate |
| CO | Carbon Monoxide |
| HNO2 | Nitrous Acid |
| H2O2 | Hydrogen Peroxide |
| HNO3 | Nitric Acid |
| NOXY | Sum of NO, NO2, and N2O5 |
| ISOP | Isoprene (5 carbons) |
| TERP | Terpenes (10 carbons) |
| ETOH | Ethanol (2 carbons) |
| SO2 | Sulfur Dioxide |
| SULF | Sulfate |
| ALDX | Higher Aldehydes (chemistry > 2, but mass of only 2 carbons) |
| IOLE | Internal olefins (4 carbons) |
| PANX | Higher Peroxyacyl Nitrates (3 carbons) |
| CH4 | Methane (1 carbon) |
| ISPD | Isoprene product |

| Steady State Species | Description |
| --- | --- |
| O | Oxygen atom (O3P) |
| O1D | Oxygen atom (O1D) |
| NO3 | Nitrate radical |
| N2O5 | Dinitrogen Pentoxide |
| OH | Hydroxyl Radical |
| HO2 | Hydroperoxyl Radical |
| XO2 | Peroxy operator (NO to NO2) |
| XO2N | Peroxy operator (NO to organic nitrate) |
| C2O3 | Peroxyacetyl Radical |
| CXO3 | Higher Peroxyacyl Radicals |
| ROR | Peroxy Radical in paraffin chemistry |
| TO2 | Peroxy Radical in aromatic chemistry |
| CRO | Peroxy Radical in cresol chemistry |

Table 6-2a. Summary of model performance metrics and statistics
for 1-hour ozone for the 12 km UAM-V modeling domain (Grid 2): base-case simulation.

Shading indicates that the calculated statistical measure is outside the EPA recommended range for acceptable model performance.
(Source: Douglas et al., 2001)

| Simulation Day | Maximum Observed Ozone (ppb) | Maximum Simulated Ozone (ppb) | Mean Observed Ozone (ppb) | Mean Simulated Ozone (ppb) | Unpaired Accuracy of the Peak (%) | Average Accuracy of the Peak (%) | Normalized Bias (%) | Normalized Gross Error (%) | RMS Error (ppb) |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 970910 | 134.0 | 101.9 | 53.8 | 47.3 | -23.9 | -7.4 | -9.3 | 22.0 | 23.0 |
| 970911 | 176.0 | 115.9 | 58.0 | 53.8 | -34.2 | -5.6 | -4.4 | 18.1 | 19.1 |
| 970912 | 123.0 | 137.1 | 62.6 | 54.4 | 11.4 | -11.5 | -11.7 | 22.3 | 22.0 |
| 970913 | 126.0 | 133.5 | 63.4 | 57.1 | 5.9 | -2.9 | -8.0 | 26.8 | 25.9 |
| 970914 | 144.0 | 151.0 | 64.2 | 55.0 | 4.8 | -1.9 | -10.6 | 30.3 | 29.7 |
| 970915 | 198.0 | 146.5 | 66.0 | 56.1 | -26.0 | -11.4 | -12.0 | 25.1 | 25.3 |
| 970916 | 135.0 | 138.8 | 65.9 | 59.6 | 2.8 | -2.4 | -7.4 | 23.1 | 22.1 |
| 970917 | 126.0 | 156.5 | 63.0 | 61.6 | 24.2 | 4.6 | 1.0 | 23.9 | 23.0 |
| 970918 | 135.0 | 151.4 | 61.7 | 65.8 | 12.1 | 7.8 | 8.9 | 23.1 | 21.9 |

Table 6-2d. Summary of model performance metrics and statistics
for 1-hour ozone for the 4 km Gulf Coast UAM-V modeling subdomain (Grid C): base-case simulation.

Shading indicates that the calculated statistical measure is outside the EPA recommended range for acceptable model performance.
(Source: Douglas et al., 2001)

| Simulation Day | Maximum Observed Ozone (ppb) | Maximum Simulated Ozone (ppb) | Mean Observed Ozone (ppb) | Mean Simulated Ozone (ppb) | Unpaired Accuracy of the Peak (%) | Average Accuracy of the Peak (%) | Normalized Bias (%) | Normalized Gross Error (%) | RMS Error (ppb) |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 970910 | 113.0 | 98.2 | 57.0 | 48.2 | -13.1 | -15.8 | -13.9 | 18.3 | 19.1 |
| 970911 | 83.0 | 115.9 | 57.2 | 49.8 | 39.6 | -14.1 | -11.9 | 16.4 | 16.9 |
| 970912 | 119.0 | 124.3 | 65.7 | 54.9 | 4.5 | -18.8 | -15.1 | 20.5 | 20.7 |
| 970913 | 126.0 | 133.5 | 64.4 | 60.8 | 5.9 | -1.5 | -3.3 | 24.7 | 23.3 |
| 970914 | 109.0 | 135.7 | 63.4 | 58.2 | 24.5 | -1.7 | -5.7 | 24.5 | 23.5 |
| 970915 | 117.0 | 146.5 | 66.8 | 52.5 | 25.2 | -16.7 | -19.9 | 28.4 | 27.8 |
| 970916 | 135.0 | 138.8 | 71.0 | 59.1 | 2.8 | -9.9 | -14.6 | 26.9 | 25.7 |
| 970917 | 126.0 | 126.0 | 64.0 | 58.1 | 0.0 | -7.0 | -5.8 | 21.1 | 21.4 |
| 970918 | 111.0 | 123.9 | 60.3 | 56.5 | 11.6 | -5.6 | -5.4 | 20.3 | 19.9 |

Table 6-2e. Summary of model performance metrics and statistics
for 1-hour ozone for the 2 km Louisiana UAM-V modeling subdomain (Grid D): base-case simulation.

Shading indicates that the calculated statistical measure is outside the EPA recommended range for acceptable model performance.
(Source: Douglas et al., 2001)

| Simulation Day | Maximum Observed Ozone (ppb) | Maximum Simulated Ozone (ppb) | Mean Observed Ozone (ppb) | Mean Simulated Ozone (ppb) | Unpaired Accuracy of the Peak (%) | Average Accuracy of the Peak (%) | Normalized Bias (%) | Normalized Gross Error (%) | RMS Error (ppb) |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 970910 | 113.0 | 91.3 | 59.0 | 49.5 | -19.2 | -14.6 | -13.7 | 21.9 | 22.8 |
| 970911 | 83.0 | 84.7 | 56.4 | 51.2 | 2.1 | -12.8 | -8.1 | 12.8 | 13.2 |
| 970912 | 119.0 | 110.3 | 67.2 | 60.4 | -7.4 | -13.2 | -8.9 | 17.0 | 16.5 |
| 970913 | 126.0 | 135.1 | 72.7 | 68.6 | 7.2 | -3.7 | -3.0 | 23.5 | 22.4 |
| 970914 | 109.0 | 126.0 | 67.3 | 58.9 | 15.6 | 4.3 | -10.8 | 26.3 | 24.2 |
| 970915 | 116.0 | 114.0 | 68.2 | 56.7 | -1.7 | -8.9 | -15.1 | 26.8 | 25.7 |
| 970916 | 135.0 | 116.4 | 77.6 | 65.3 | -13.8 | -16.9 | -13.1 | 26.7 | 25.3 |
| 970917 | 126.0 | 101.3 | 68.2 | 58.2 | -19.6 | -14.4 | -9.6 | 22.5 | 24.1 |
| 970918 | 107.0 | 108.4 | 66.6 | 61.3 | 1.3 | -5.1 | -6.8 | 19.7 | 18.9 |

Table 6-2a—CB-V. Summary of model performance metrics and statistics
for 1-hour ozone for the 12 km UAM-V modeling domain (Grid 2): base-case simulation.

Shading indicates that the calculated statistical measure is outside the EPA recommended range for acceptable model performance.

| Simulation Day | Maximum Observed Ozone (ppb) | Maximum Simulated Ozone (ppb) | Mean Observed Ozone (ppb) | Mean Simulated Ozone (ppb) | Unpaired Accuracy of the Peak (%) | Average Accuracy of the Peak (%) | Normalized Bias (%) | Normalized Gross Error (%) | RMS Error (ppb) |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 970910 | 134 | 98.3 | 53.8 | 47.0 | -26.7 | -6.4 | -9.8 | 22.5 | 18.0 |
| 970911 | 176 | 115.4 | 58.0 | 54.1 | -34.4 | -4.8 | -3.8 | 17.6 | 16.6 |
| 970912 | 123 | 130.3 | 62.6 | 55.0 | 5.9 | -8.7 | -10.7 | 21.2 | 17.2 |
| 970913 | 126 | 135.3 | 63.4 | 57.3 | 7.4 | 3.2 | -7.6 | 25.7 | 20.7 |
| 970914 | 144 | 141.6 | 64.2 | 55.7 | -1.7 | 13.9 | -9.3 | 29.0 | 24.0 |
| 970915 | 198 | 145 | 66.1 | 56.6 | -26.8 | -4.0 | -11.1 | 24.2 | 22.6 |
| 970916 | 135 | 134.4 | 65.9 | 60.4 | -0.4 | 6.3 | -6.2 | 22.0 | 17.0 |
| 970917 | 126 | 148.4 | 63.0 | 62.4 | 17.8 | 13.4 | 2.3 | 23.1 | 17.8 |
| 970918 | 135 | 147.9 | 61.7 | 66.5 | 9.6 | 11.4 | 10.4 | 22.5 | 17.2 |

Table 6-2d—CB-V. Summary of model performance metrics and statistics
for 1-hour ozone for the 4 km Gulf Coast UAM-V modeling subdomain (Grid C): base-case simulation.

Shading indicates that the calculated statistical measure is outside the EPA recommended range for acceptable model performance.

| Simulation Day | Maximum Observed Ozone (ppb) | Maximum Simulated Ozone (ppb) | Mean Observed Ozone (ppb) | Mean Simulated Ozone (ppb) | Unpaired Accuracy of the Peak (%) | Average Accuracy of the Peak (%) | Normalized Bias (%) | Normalized Gross Error (%) | RMS Error (ppb) |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 970910 | 113 | 94.7 | 57.0 | 48.1 | -16.2 | -16.1 | -14.1 | 18.6 | 15.2 |
| 970911 | 83 | 115.4 | 57.2 | 50.4 | 39.1 | -13.3 | -10.7 | 15.5 | 12.5 |
| 970912 | 119 | 123.7 | 65.7 | 55.8 | 4.0 | -17.8 | -13.6 | 19.4 | 16.0 |
| 970913 | 126 | 135.3 | 64.4 | 61.7 | 7.4 | -0.3 | -1.9 | 23.9 | 18.7 |
| 970914 | 109 | 134.8 | 63.4 | 59.9 | 23.7 | 0.1 | -2.8 | 23.2 | 16.8 |
| 970915 | 117 | 145 | 66.8 | 53.6 | 23.9 | -16.6 | -17.9 | 26.9 | 22.4 |
| 970916 | 135 | 134.4 | 71.0 | 59.8 | -0.4 | -10.1 | -13.6 | 26.0 | 20.9 |
| 970917 | 126 | 122.8 | 64.0 | 59.4 | -2.5 | 4.4 | -3.7 | 20.7 | 17.6 |
| 970918 | 111 | 123.9 | 60.3 | 58.5 | 11.6 | -2.5 | -1.6 | 19.5 | 15.2 |

Table 6-2e—CB-V. Summary of model performance metrics and statistics
for 1-hour ozone for the 2 km Louisiana UAM-V modeling subdomain (Grid D): base-case simulation.

Shading indicates that the calculated statistical measure is outside the EPA recommended range for acceptable model performance.

| Simulation Day | Maximum Observed Ozone (ppb) | Maximum Simulated Ozone (ppb) | Mean Observed Ozone (ppb) | Mean Simulated Ozone (ppb) | Unpaired Accuracy of the Peak (%) | Average Accuracy of the Peak (%) | Normalized Bias (%) | Normalized Gross Error (%) | RMS Error (ppb) |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 970910 | 113 | 91.1 | 59.0 | 49.4 | -19.3 | -15.0 | -13.9 | 22.3 | 17.5 |
| 970911 | 83 | 84.4 | 56.4 | 51.3 | 1.6 | -12.3 | -7.8 | 12.6 | 9.1 |
| 970912 | 119 | 109.9 | 67.2 | 60.7 | -7.6 | -13.0 | -8.6 | 16.3 | 13.7 |
| 970913 | 126 | 129.8 | 72.7 | 69.1 | 3.0 | -3.4 | -2.3 | 22.4 | 19.3 |
| 970914 | 109 | 127.4 | 67.3 | 60.4 | 16.9 | 5.1 | -8.6 | 24.0 | 19.1 |
| 970915 | 116 | 114.8 | 68.2 | 59.2 | -1.0 | -7.2 | -11.2 | 24.0 | 21.1 |
| 970916 | 135 | 114.8 | 77.6 | 65.1 | -14.9 | -18.2 | -13.2 | 26.7 | 23.1 |
| 970917 | 126 | 102.4 | 68.2 | 59.7 | -18.7 | -13.0 | -7.3 | 22.2 | 21.2 |
| 970918 | 107 | 107.2 | 66.6 | 62.6 | 0.2 | -4.2 | -4.8 | 19.0 | 15.9 |

Figure 1. GCOS UAM-V modeling domain. Horizontal grid resolution is approximately 36 km for Grid 1, 12 km for Grid 2, 4 km for Grids A, B, and C, and 2 km for Grid D.

Figure 2. Hourly ozone concentrations (ppb): CB-V vs. CB-IVtox for September 13–16, 1997

This page intentionally left blank.

# Footnotes

See http://airsite.unc.edu/soft/cb4/CB4docs.html